## Slide 1
Subject Name:- Microprocessor & Microcontroller
Subject Code:- KEC-502
Unit No.:- 5
Lecture No.:- 1
Topic Name :- 8051 Microcontroller Instruction Set
Er. Preeti Verma
ECE Department

## Slide 2
8051 Microcontroller Instruction Set
Any instruction given to the microcontroller contains two parts: an opcode and an operand.
The opcode is responsible for telling the microcontroller what to do, whereas the operand holds the data on which the operations are to be performed.
The 8051 microcontroller has an 8-bit opcode which gives it the ability to handle 2^8(256) instructions.
The operands, on the other hand, can be of 0 bytes, 1 byte or 2 bytes.
Type of instruction:
    Data transfer
    Arithmetic
    Logical
    Bit Manipulation
    Program branching

## Slide 3
Data Transfer Instructions
The Data Transfer Instructions are associated with transfer with data between registers or external program memory or external data memory. The Mnemonics associated with Data Transfer are given below.
    MOV
    MOVC
    MOVX
    PUSH
    POP
    XCH
    XCHD

## Slide 4
MOV Instruction
The MOV instruction has two operands, the source, and the destination. The second operand is the source, whereas the first one is the destination. This instruction uses various addressing modes to move data in the RAM space of the microcontroller.
Data transfer instructions are responsible for transferring data between various memory storing elements like registers, RAM, and ROM. The execution time of these instructions varies based on how complex an operation they have to perform. In the table given below, we have listed all the data transfer instruction. In the table [A]= Accumulator; [Rn]=Register in RAM; DPTR=Data Pointer; PC=Program Counter

## Slide 5
MOV R5,#0F9H In this instruction 0 is used between # and F to indicate that F is a hex number and not a letter .In other word “MOV R5, #F9” Will cause a error.
If the value 0 to F move in 8 bit register , the rest of bit are assume to be zero. For example in “MOV A, #5” the result will be A=05
Data to Register

## Slide 6
Write instruction to use register bank 0,and load same value 05H in registers R0 to R2
                MOV R0, # 05H
                MOV R1, #05H
                MOV R2, #05H
Write instruction to use register bank 3,and load same value 05H in registers R0 to R2
                SETB PSW.4
                SETB PSW.3
                MOV R0, # 05H
                MOV R1, #05H
                MOV R2, #05H

## Slide 7
Data to Memory
Write a program to copy the value 55H into RAM memory location 40H to 42H using direct and indirect mode.
Direct Mode
                MOV 40, #55H
                MOV 41, #55H
                MOV 42, #55H

## Slide 8
b) Indirect
              MOV R0, 40
              MOV @R0, #55H
              INC R0
              MOV @R0, #55H
              INC R0
              MOV @R0, #55H

## Slide 9
Register to Register
It should be noted that source and destination registers must be match in size. In other words , coding MOV DPTR, A will give an error, since the source is 8 bit register and destination is 16 bit register.
We can move data between A and Rn(n=0 to7)but movement of data between Rn register is not allowed. For example instruction “MOV R4,R7” is invalid.

## Slide 10
Memory to register
Write instruction to copy the content of memory location(46) in register A, using direct and indirect addressing mode.
Indirect
    MOV R0, #46
    MOV A,@R0
b) Direct
MOV A, 46

## Slide 11
Address to Address

## Slide 12
MOVC Instruction
MOVC moves a byte from Code Memory into the Accumulator. The Code Memory address from which the byte will be moved is calculated by summing the value of the Accumulator with either DPTR or the Program Counter (PC).
In the case of the Program Counter, PC is first incremented by 1 before being summed with the Accumulator.
Opcode | Operand | Description
MOVC | A, @A+DPTR | Moves data to accumulator from a address stored in the memory location (internal ROM) at A+DPTR
 | A, @A+PC | Moves data to accumulator from a address stored in the memory location(internal ROM) at A+PC

## Slide 13
MOVX Instruction
The MOVX instruction transfers data between the accumulator and external data memory. External memory may be addressed via 16-bits in the DPTR register or via 8-bits in the R0 or R1 registers. When using 8-bit addressing, Port 2 must contain the high-order byte of the address.
Opcode | Operand | Description
MOVX | @DPTR,A | If operand1 is @DPTR, the Accumulator is moved to the 16-bit External Memory address indicated by DPTR.
 | @R0,A | If operand1 is @R0 the Accumulator is moved to the 8-bit External Memory address indicated by R0.
 | @R1,A | If operand1 is @R1, the Accumulator is moved to the 16-bit External Memory address indicated by R1.
 | A,@DPTR | This instruction move 8-bit data of external memory in accumulator , location is given by DPTR
 | A,@R0 | This instruction move 8-bit data of external memory in accumulator , location is given by R0

## Slide 14
Important Questions
What are the instruction format available in 8051?
Which instruction of 8051 is not permitted?
What type of instruction is swap?
What is the operation of pop instruction?
When push instruction is executed?

## Slide 15
References
Text Books:
Mazidi Ali Muhammad, Mazidi Gillispie Janice, and McKinlay Rolin D., “The 8051 Microcontroller and Embedded Systems using Assembly and C”, Pearson, 2nd Edition,2006
Shah Satish, “8051 Microcontrollers MCS 51 Family and its variants”, Oxford,2010
Reference Books:
1. V. Udayashankara, M.S. Mallikajunaswamy, “8051 Microcontroller Hardware, Software and Applications”, McGraw-Hill, 2017

## Slide 16
Thank You