## Slide 1
Subject Name:- Microprocessor & Microcontroller
Subject Code:- KEC-502
Unit No.:- 5
Lecture No.:- 3
Topic Name :-Single bit Instructions , Arithmetic Instructions
Er. Preeti Verma
ECE Department

## Slide 2
Single bit Instructions
8051 has a powerful function ：8051 allows programmer to access a single bit (not a byte) on the RAM or register. This type of accessing method is called bit-addressable
The bit-addressing mode can only provide on specific area of the RAM (20H-3FH) or some specified registers.
I/O: all ports are bit-addressable
Instruction | Function
SETB bit | Set the bit (bit=1)
CLR bit | Clear the bit (bit=0)
CPL bit | Complement the bit
JB bit ,target | Jump to the target if bit =1
JNB bit , target | Jump to the target if bit =0
JBC bit, target | Jump to the target if bit =1,Clear bit

## Slide 3
Ex: Write a program to perform the following –
    Keep monitoring the P1.2 bit until it becomes high
    When P1.2 becomes high, write value 45H to P0, and
    Send a high-to-low pulse to P2.3
  SETB P1.2
  Back: JNB P1.2, Back
  MOV A,#45H
  MOV P0,A
  SETB P2.3
  CLRB P2.3

## Slide 4
Ex: A Switch is connected to pin P1.7. Write a program to check the status of the SW and perform the following:
  If SW=0, Send letter ‘N’ to P2
  If SW=1, Send letter ‘Y’ to P2
  SETB P1.7
  Again: JB P1.7, Over
  MOV A,# ‘N’
  MOV P2,A
  SJMP Again
Over: MOV A,# ‘Y’
  MOV P2,A
  SJMP Again

## Slide 5
Arithmetic Instructions
In 8051 Microcontroller there are 24 different instructions under the Arithmetic Group.
In total there are 64 opcodes. The Carry Flag (CY), Auxiliary Carry (AC)and Overflow flag (OV) are affected based on the result of ADD, ADDC, SUBB etc. instructions.
The multiple and divide instructions clear the Carry flag, and also does not affect the AC flag. After execution of multiplication, the OV flag will be 1 when the result is greater than FFH. Otherwise, it is 0.
Similarly, after division OV flag is 1 when the content of B is 00H before division, otherwise it is 0.
The DA A (Decimal Adjust Accumulator) affects the Carry Flag only.

## Slide 6
Operation | Opcode | Operand | Description
Addition | ADD | A, Rn | [A]=[A]+[Rn]
 | ADD | A, Address | [A]=[A]+[ Data at Address]
 | ADD | A, @Rn | [A]=[A]+[ Data at Address pointed by Rn ]
 | ADD | A, #data | [A] =[A]+[Data]
 | ADDC | A, Rn | [A]=[A]+[Rn]+[Carry flag]
 | ADDC | A, Address | [A]=[A]+[ Data at Address]+[Carry flag]
 | ADDC | A, @Rn | [A]=[A]+[ Data at Address pointed by Rn]+[Carry flag]
 | ADDC | A, #data | [A]=[A]+[Data]]+[Carry flag]
Addition Instructions

## Slide 7
Ex: Assume that RAM location 40-44 have the values . Write a program to find the sum of the value. At the end of the program , register A should contain the lower byte and R7 the higher byte
MOV R0,#40H
MOV R1,#05H
CLR A
MOV R7,A
Back: ADD A,@R0
JNC Next
INC R7
Next: INC R0
DJNZ Back

## Slide 8
Write a program to
Add two 16- bit numbers, the numbers are FC45H and 02ECH
Add two 32 –bit numbers, the numbers are stored in memory locations
Address | Data
40H | C0H
41H | 2BH
42H | 45H
43H | 01H
Address | Data
50H | FEH
51H | 05H
52H | C7H
53H | 56H
Program
CLR C
MVI A, # 45H
ADD A,#0ECH
MOV R0,A
MVI A, #0FCH
ADDC A, #02H
MOV R1,A

## Slide 9
Address | Data
40H | C0H
41H | 2BH
42H | 45H
43H | 01H
Address | Data
50H | FEH
51H | 05H
52H | C7H
53H | 56H
Address | Data
60H | BEH
61H | 05H
62H | C7H
63H | 56H
Result
b) Program
MOV R3,#04H
CLR C
MOV R0, #40H
MOV R1, #50H
SETB PSW.3
MOV R0,#60H
CLR PSW.3
Back: MOV A,@R0
ADDC A,@R1
SETB PSW.3
MOV @R0,A
INC R0
CLR PSW.3
INC R0
INC R1
DJNZ R3 Back

## Slide 10
Subtraction | Opcode | Operand | Description
 | SUBB | A, Rn | [A]<-[A]-[Rn]
 | SUBB | A, Address | [A]<-[A]-[ Data at Address]
 | SUBB | A, @Rn | [A]<-[A]-[ Data at Address pointed by Rn ]
 | SUBB | A, #data | [A]<-[A]-[Data]
Subtraction Instructions

## Slide 11
Operation | Opcode | Operand | Description
Multiplication | MUL | A,B | [A]=[A]*[B]
Division | DIV | A,B | [A]=[A]/[B]
Decimal adjust | DA | A | Coverts binary addition to BCD
Multiplication, Division and Decimal adjust Instructions
In case of multiplication one operand should we in register A and second operand must be in register B. After multiplication result in register A and B; the lower byte in A and upper byte in register B.
In case of divide , the numerator must be in register A and the denominator must be in register B. after divide the quotient is in register A and remainder in register B.
The divide instruction always makes CY=0 and OV=0 if denominator is not zero. If denominator zero (B=0) ,OV=1,indicate an error and CY=0.

## Slide 12
Ex: In a semester exam, student has taken six courses. The marks of the student ( out of 25 ) and store in RAM locations 47H onwards. Find the average marks, and output it on port 1.
MOV R0,# 47H
MOV B,#06H
MOV R1,#06
MOV A,#00H
Back: ADD A,@R0
INC R0
DJNZ Back
DIV AB
MOV P1,A

## Slide 13
Important Questions
State the step that the SUBB instruction will go through each of the following
a) 23H-12H b) 43H-53H c) 99H -99H
What is arithmetic and logic instructions?
Write a program to add all the digit in your ID number and save result in R3 register.
Which flag is affected by MUL and DIV?
Which register is used by multiply and divide instruction?

## Slide 14
References
Text Books:
Mazidi Ali Muhammad, Mazidi Gillispie Janice, and McKinlay Rolin D., “The 8051 Microcontroller and Embedded Systems using Assembly and C”, Pearson, 2nd Edition,2006
Shah Satish, “8051 Microcontrollers MCS 51 Family and its variants”, Oxford,2010
Reference Books:
1. V. Udayashankara, M.S. Mallikajunaswamy, “8051 Microcontroller Hardware, Software and Applications”, McGraw-Hill, 2017

## Slide 15
Thank You